Victor Reader Stream What's New

Version 3.3 Release Notes

# Installation

## Using HumanWare Companion

If you have HumanWare Companion 3.3 or higher installed on your computer, you may use it to update your Stream player with the new software version. To do this:

- Connect your Stream to your computer or place your Stream SD card into the computer SD card reader.

- On the Companion Help menu, select "Check for Stream Update".

- A dialog will open and check your Stream software version. If your Stream software is not up to date, the dialog will display the latest version number that is available along with a brief list of new features.

- To update your Stream, select the Install New Version button. Note: If Companion cannot detect your Stream version number, you may still select the Install button and proceed with the upgrade. The Companion will then download the Stream software from HumanWare and transfer it to your Stream SD card.

- Disconnect your Stream from the computer or reinsert the SD card back into your Stream.

- Connect the Stream to a power outlet and power it on.

- The software update will start automatically. The installation process takes about 1 minute, during which time the Stream will issue periodic "Please wait" messages. The Stream will announce when the update is complete and then it will power off.

- When you power the Stream back on you can confirm the new version number by pressing the INFO key 0.

## Download from HumanWare

If you do not use the Companion program you may download the latest software from HumanWare. It may be downloaded from:

http://www.humanware.com/stream_software

Also, you may wish to visit the Stream support page at:

http://www.humanware.com/stream_support

Here you will find additional resources including the Stream User Guide, FAQ, tutorials, and a link listing samples of “Where to find content for your Stream”.

After you install the new software, this Release Notes document you are now reading will also be saved to a HumanWare folder in the text bookshelf on your Stream SD card.

Software Installation Instructions:

The update software is a single file ending in .UPG. It is contained in the downloaded zip file. To update your Stream:

- Download the software zip file from HumanWare at the above link.

- Unzip the .UPG file and copy it to the root of an SD card. Note that you do not need to install special unzip software. Windows will unzip the UPG file. Simply press ENTER on the zip file and the UPG file will appear. Then press the SPACEBAR to select the UPG file and press CONTROL+C to copy it to the clipboard. Then navigate to the root of your Stream SD card and press CONTROL+V to paste the UPG file from the clipboard to the root of the SD card.

- Connect the Stream to a power outlet and power it on.

- The software update will start automatically. The installation process takes about 1 minute during which time the Stream will issue periodic “Please wait” messages. The Stream will announce when the update is complete and then it will power off.

- When you power the Stream back on you can confirm the new version number by pressing the INFO key 0.

# New Features

- Support of new Japanese and Chinese text-to-speech voices.

- CD Accessory: If you use the Stream CD drive accessory, you can now play and copy MP3 CD books. The MP3 books will be copied to the Stream Other Books bookshelf. You can also play (but not copy) a commercial audio CD.

- Announce Author for NISO Books: For DAISY 3 NISO books such as those from NLS, if the author metadata has been provided by the book producer, then the author will be announced when browsing the bookshelf or pressing the INFO key 0.

- Spell Mode: When you use the 2/8 keys to navigate to the Spell Word function, the Stream will now automatically spell the current word. You can then use keys 4/6 as before to spell the previous or next word.

- More accurate messages containing numbers: The Stream messages containing numbers are now more precise with respect to plurals and genders in some languages. For example, in English Stream will now announce, "0 bookmarks" instead of "0 bookmark".

- PC Disconnect. When you disconnect the Stream from the PC it will now automatically power off. This is because after disconnecting from the PC, it is necessary to power off and back on again before you can use the Stream.

- Stream Attributes file: When you begin using Stream 3.3 you may notice a file created on your SD card with the name, $VRStream_Attributes. Please ignore this file and do not edit it. It is used to provide player information to the HumanWare Companion program. If you need to format your SD card it is ok. The Stream will re-create this file if it is not on the card.

# Issues Corrected

- DOCX: Corrections have been made that prevented some DOCX documents from playing. DOCX files can only be played on Streams that have the Stream SoftPak installed.

- DAISY NISO Text-only Books: Some NISO text-only books with html list tags could crash the Stream. This issue has been corrected.

- DAISY Books with Space at end of Title: If you tried to copy a DAISY book from the CD accessory or from a USB stick (such as an NLS cartridge) and that book had a space at the end of the title, a media error 12 would occur. This issue has been corrected.

- Large Text Books: The Stream is now able to play large DAISY text-only books such as those from Bookshare.org. Note that you may hear “Please Wait” messages when opening these books while Stream scans the large book structure.

- If you had both audio files and folders within a sub-folder of $VROtherBooks the Stream would not always find the audio files. This has been corrected.

[End of document Revision 6-20101029]